## Slide 1: Stream Sampling for Benthic Macroinvertebrates
What are the bugs telling us?
And who understands them?
Presented By:
Grant De Jong
Rocky Mountain Water Quality Analysts Association
2014 Annual Symposium
April 25, 2014

## Slide 2: “Benthic Macroinvertebrates”? “Bugs”?
This?
This?
Heteroptera?
An aquatic, multicellular animal without a backbone and large enough to be seen with the naked eye.

## Slide 3: Who are they?

## Slide 4: Step 1 – Collect your bugs

## Slide 5: Kick Net (qualitative, or, at best, semi-quantitative)
This is the “kick net” some people use
This is the kick net I prefer to use
  Use it to sample habitat other than riffles

## Slide 6
Qualitative – presence/absence, maybe some relative abundance
  Gives us a “Who’s there” approach
  Not generally amenable to statistical analysis
Quantitative – numbers
  Usually reported in #/m2
Replication
  Gives us ability to run statistics
    ANOVA, t-tests, etc.

## Slide 7: Hess sampler
Originally designed for use in soft-bottom streams in the East.
Steve Canton and Jim Chadwick modified it for the cobble-bottom streams of Colorado and the West.

## Slide 8: Colorado State Protocol
Uses a semi-quantitative approach:
  1 kick net sample in 1 m² of riffle habitat over 60 seconds
Since this was done at 100’s of sites, the data can be used in a regional approach
Individual sites can be compared to the region, but not to each other

## Slide 9: Step 2: Lab work
Samples come to the lab filled with
  Sticks
  Stones
  Grass
  Algae
  Mud
  Sand
  Unidentifiable
  plastic stuff
  and Bugs!
Someone gets to sort the bugs from all that debris.

## Slide 10
and then identify all those bugs
and
count
them.

## Slide 11: Invertebrate Taxonomy
Bugs from the samples are identified – usually to the genus or species level.
Quality assurance on IDs and counts – 95% is pass level
Report lists all of the taxa and their counts for each replicate at each site.

## Slide 12: Final Bug Report
INSECTA
  EPHEMEROPTERA
    Baetis bicaudatus
    Paraleptophlebia sp.
    Timpanoga hecuba
  ODONATA
    Archilestes sp.
    Enallagma sp.
  PLECOPTERA
    Cultus aestivalis
    Doroneuria baumanni
    Skwala paralella
    Sweltsa sp.
  COLEOPTERA
    Agabus sp.
  TRICHOPTERA
    Arctopsyche grandis
    Hesperophylax sp.
    Hydropsyche sp.
    Rhyacophila brunnea/vao
  DIPTERA
    Ceratopogoninae
    Neoplasta sp.
    Simulium sp.
CRUSTACEA
  AMPHIPODA
    Hyalella azteca cx.
MOLLUSCA
  PELECYPODA
    Dreissena polymorpha

## Slide 13: Final Bug Report
Several metrics automatically calculated on a replicate basis (therefore, we can use them for statistical analysis)
  Total density
  Number of taxa
  Number of EPT taxa
  EPT Index
  Ephemeroptera Abundance
Some metrics calculated based on composite of replicates
  All above metrics
  Shannon-Weaver Diversity Index
  Additional metrics

## Slide 14: Translating the Data
Our “Universal Translator” – takes bug names and translates them into ecological entities
BUGSWITH, GEI’s in-house, proprietary system in Excel for managing invertebrate data
  Benthic Invert Taxa List
  Data Entry/Report Production Worksheets
  Taxon Characterization Worksheet
  Metric Calculation Worksheet
  List of Taxonomic Literature
  Data can be used to calculate Colorado Multimetric Index (MMI)

## Slide 15: Benthic Invert Taxa List - the “backbone” of the system
List of 12,337 invertebrate taxa (1 January 2014)
  Started with <2,000 taxa, using Barbour et al. (1999)
  Taxa added as we encounter checklists or taxonomic revisions
  Total of 10,491 (85%) are insect taxa
Features:
  Standard Taxonomic Effort
  Taxonomic Serial Numbers
  Tolerance Values
  Species Traits
  Geographic Distribution
Supported by >670 pieces of literature (books, articles, etc.)

## Slide 16: Standard Taxonomic Effort
Indicates standard taxonomic level to stop at when identifying invertebrates
  Usually genus level
  Some species level
  Sometimes family or subfamily level
Indicates appropriate literature to use
Identifies monospecific genera at Nearctic, regional, or state levels
Identifies synonyms, so proper name can be used
Includes some distributional information

## Slide 17: Taxonomic Serial Numbers
TSNs are unique numbers assigned to each taxon
U.S. Department of Agriculture
  Integrated Taxonomic Information System
  Standardized identification system

## Slide 18: Tolerance Values
Based on Saprobien System of early 1900s
Chutter (1972) first to assign tolerance values
Hilsenhoff Biotic Index (HBI - 1977)
  Wisconsin
  Designed to identify organic pollution
  Values based mostly on professional experience
Some at Family level, but generally use genus and species level TVs

## Slide 19: Tolerance Values
0 - Pristine
10 - Degraded
TV
0 – 3
Intolerant
4 – 6
Moderate
7 – 10
Tolerant

## Slide 20: Hilsenhoff Biotic Index
HBI = Σ (density * TV) / Total Density
Taxon | Density | TV | Density x TV
Baetis tricaudatus | 100 | 4 | 400
Rhyacophila sp. | 25 | 0 | 0
Chironomus sp. | 50 | 8 | 400
Total Density | 175 |  | Σ TV = 800
HBI = 800/175 = 4.57 |  |  |